## Slide 1: מבוא לרשתות
תחזוקת PC

## Slide 2: Network Types
Local Area Network
Wide Area Network
Wireless Network
  Cellular
  Wireless LAN
Personal Area Network
  Bluetooth
  Wireless Mouse & Keyboard

## Slide 3: Local Area Network
A Single Building to a Campus
Radius 1m – 2-3 Km
Very High Bandwidth > 1Gbps
Immediate Access Services
  File Access
  Printing
  E-Mail
  Intranet

## Slide 4: Local Area Network 2
Single Management
Ethernet Infrastructure
Local Maintenance
Usually 2 Level of LANs
  Core Network
    Connects Servers, Storage, etc…
  Access Network
    Connects Workstations

## Slide 5: Wide Area Network
Between Branches / Business Partners
Country wide to Global in scope – 20,000 Km
Medium Bandwidth 1-100 Mbps
Non Time-Critical Services
  File Download / Upload
  E-Mail
  Intranet
  Internet Access

## Slide 6: Wide Area Network 2
Hierarchical Management
  Each Site may be managed independently
  Infrastructure managed by ISP/Operator
MPLS & Other ISP Infrastructure
Distributed Maintenance

## Slide 7: Wireless Networks

## Slide 8: תקנים לרשתות אלחוטיות

## Slide 9: IEEE 802
IEEE – International Electric & Electronic Engineers
תקני רשת – משפחת 802
  http://www.ieee802.org
  https://ieeexplore.ieee.org/browse/standards/get-program/page/series?id=68

## Slide 10: Wireless LAN
Office to a Floor
Radius < 30m
Low to Medium Bandwidth
Lan Services
Standard | Theoretical | Actual
802.11b | 11 Mbps | 5.5 Mbps
802.11a | 54 Mbps | 20 Mbps
802.11g | 54 Mbps | 20 Mbps
802.11n | 300 Mbps | 100 Mbps
802.11ac | 7,000 Mbps | 2,100 Mbps

## Slide 11: Wireless Network - Cellular
Protocols based on 3GPP
  3rd Generation Partnership Project
  ARIB, ATIS, CCSA, ETSI, TSDSI, TTA, TTC
Cell Radius varies
Relatively Low Bandwidth < 100Mbps
Internet Services
Mobile Network Operator provides Internet Connectivity

## Slide 12: Personal Area Networks (Bluetooth)
Desk Area, Person’s Body, Car
Radius < 3m
Very Low Bandwidth < 1Mbps
Smartphones, Tablets, Laptops
Device Connectivity Services
  Audio
  Phone Control
  Input Devices
  House Alarm Sensors

## Slide 13: דורות סלולאריים
דור ראשון
  שנות ה-80 של המאה העשרים
  קול אנלוגי
דור שני
  שנות ה-90 של המאה העשרים
  קול דיגיטלי
דור שלישי
  סביב 2010
  נתונים דיגיטליים
  שירותי מיקום
דור רביעי
  סביב 2015
  וידאו

## Slide 14: כמה מילים על הדור החמישי 5G